## Slide 1
ThermalSight v1.8.0
Foot Thermal Image Processing & Diagnostic Workflow
A Simple & Clear Guide: From FLIR Thermal Camera Capture to Ready-to-Publish Medical Analysis
Designed for high clarity, large legibility, and straightforward understanding for senior audiences, physicians, and professors.

## Slide 2
STEP 1 Input Data: What Goes Into the System?
The types of thermal images accepted by ThermalSight
1. FLIR Thermal Images
• Uses genuine radiometric images from FLIR cameras (.jpg, .png, or .tiff). • These are not ordinary photos: every pixel carries true, calibrated physical temperature values in degrees Celsius.
2. Flexible Input Modes
• Single Image Mode: Select 1 photo for instant inspection. • Sequence Folder Mode: Select an entire folder containing 10–50 consecutive patient walk/treadmill images. • Or simply Drag & Drop files directly onto the screen.
3. Smart Root Filter
• If the folder contains previous result subfolders (_Result or _analysis), the app automatically ignores them. • Only primary patient photos in the root folder are loaded, preventing any duplicate or mixed data.

## Slide 3
STEP 2 FLIR Image Cleaning (Pure Radiometric Sensor)
How the system extracts clean, natural foot images without artificial blur
The Problem: Camera Stamps & Overlays
FLIR cameras burn unwanted visual accessories onto pictures: • Temperature text badges (e.g., '35.0 °C' in the top corner) • Company branding logo ('FLIR' in the bottom corner) • Right-side vertical color scale bar (colorbar) • Center crosshair / reticle mark If erased using ordinary image patching (blur / inpaint), the foot boundaries become fuzzy, distorted, and clinically unreliable.
The v1.8.0 Solution: Pure Sensor Extraction
ThermalSight decodes raw 16-bit sensor bytes directly using Planck radiometric equations (via 'flyr'): ✓ Zero artificial blurring or pixel patching. ✓ Logos, 35°C badges, and colorbars vanish naturally at byte level. ✓ 100% of physical sensor accuracy is preserved bit-for-bit. Result: You get a completely pristine, crystal-clear thermal foot image ready for precise measurement.

## Slide 4
STEP 3 Application Workflow (4 Practical Stages)
The simple step-by-step user journey from start to finish
STAGE 1 Upload Images
Open 1 single photo or an entire sequence folder. The system safely reads and validates all files with a clear progress bar.
STAGE 2 Calibrate Scale
Draw a box over a reference card (e.g., 10×10 cm) or ruler line. Purpose: Matches computer screen pixels exactly to real human anatomy (px to cm).
STAGE 3 Mark Foot Points
Single-click on clinical landmarks (e.g., big toe or ball of foot). A standardized circle forms instantly and heat spread direction is calculated.
STAGE 4 Save & Export
Click 'Save & Export'. The app automatically compiles journal-quality figures, numeric CSV spreadsheets, and a ZIP archive.

## Slide 5
STEP 4 9×9 Grid Standardization
How circular observation windows are standardized and why 9×9 cells matter
1. Exact 9×9 Cell Dimension
• In clinical research, the plantar sole is mapped onto a uniform geometric grid. • Each landmark circle is locked to exactly 9 grid cells in diameter (radius = 4.5 cells). • Purpose: Guarantees that temperature readings and heat-flux calculations are fair, uniform, and reproducible across all patients.
2. Dynamic Distance Sync
• Camera distance can vary between photo sessions (some taken closer, some farther away). • Thanks to initial scale calibration, the app dynamically scales the screen pixels. • The real physical size on the patient's skin stays perfectly constant: exactly 1.2 cm.
3. Seamless Auto-Upgrade
• If you open an older session file (v1.6 / v1.7) where circles were smaller (e.g. 6×6): ✓ The app automatically rescales them to the 9×9 standard. ✓ Landmark center points (cx, cy) stay 100% frozen in place. ✓ Historical research data is upgraded instantly without redrawing!

## Slide 6
STEP 5 Final Deliverables & Results (Output Package)
The complete set of scientific charts, images, and tables produced
1. Journal Publication Figures (Figure 1)
• High-contrast monochrome (white-hot) foot background. • High-resolution false-color (Ironbow) thermal circles inside ROIs. • Precision hairline grid overlays meeting journal standards.
2. Directional Heat Spread Maps (Compass)
• Samples thermal propagation along 8 compass directions (N, NE, E, SE, S, SW, W, NW). • Vectors and radar rose reveal dominant heat-flow drift across the foot.
3. Comprehensive Tabular Metrics (CSV / Excel)
• Tabulates maximum, minimum, and mean temperatures per landmark. • Records physical pixel-to-cm calibration ratios for medical audit trails.
4. 1-Click Portable Archive (ZIP & JSON)
• Bundles all figures, vector maps, and spreadsheets into 1 structured ZIP archive. • Portable session backup (.json) allows resuming work anytime without data loss.